TA45 SERIES A.C. TUBULAR MOTOR

Motor Characteristic

TA45 series A.C. tubular motors fit all kinds of electric roller blinds, canopies, Roman blinds, Venetian blinds, projection screens, awnings, and outside solar protections.

The product has complete overheat and overload protections. Insure the motor against accident, we produce the motor with inflame retardant materials. In order to reduce noise, shake and supply complete guarantee for it’s use life, we adopted sealed lubricate design for the structure components. In order to setting exact orientation, we designed exact mechanical travel control. Over-narrow bracket design furthest reduce the space between the fabric and the wall.

Attention

Please read this manual carefully before install or use.

Please install this product by professional people.

Never hit the motor, or tear down the motor.

Do not add lubricant on the motor or any components.

Motor Specification

| Model | Voltage (V) | Frequency (Hz) | Current (A) | Power (W) | Torque (Nm) | Speed (rpm) | Travel (Turns) | Noise (dB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TA45-6/22 | 100-120 | 50/60 | 0.4 | 90 | 6 | 22/26 | 32 | ＜45 |
| TA45-6/22-L | 100-120 | 50/60 | 0.4 | 90 | 6 | 22/26 | 42 | ＜45 |
| TA45-8/17 | 100-120 | 50/60 | 0.4 | 90 | 8 | 17/20 | 32 | ＜45 |
| TA45-8/17-L | 100-120 | 50/60 | 0.4 | 90 | 8 | 17/20 | 42 | ＜45 |
| TA45-12/22 | 100-120 | 50/60 | 0.65 | 140 | 12 | 22/26 | 32 | ＜45 |
| TA45-12/22-L | 100-120 | 50/60 | 0.65 | 140 | 12 | 22/26 | 42 | ＜45 |
| TA45-15/17 | 100-120 | 50/60 | 0.65 | 140 | 15 | 17/20 | 32 | ＜45 |
| TA45-15/17-L | 100-120 | 50/60 | 0.65 | 140 | 15 | 17/20 | 42 | ＜45 |
| Insulation class Class F Protection index IP44 Overheating protection 6 min |

System Accessories

|  | Motor bracket 323505 |  |  | 180° bracket 323510 |
| --- | --- | --- | --- | --- |
|  | Idler bracket 323506 |  |  | 135° bracket 323509 |
|  | Ф50 wheel 323504 |  |  | 90° bracket 323508 |
|  | Ф50 roller tube 323503 |  |  | Travel stick 323507 |

System Installation

| Machining the slot on the roller tube When use Ф50 roller tube, it must cut a slot on the roller tube (Drawing 1). The slot is used to connect the motor turning ring. | Drawing 1 Drawing 3 Drawing 5 Drawing 7 |
| --- | --- |
| Connect the motor and roller tube 1. (Drawing 2) Drill a hole on the roller tube, fix the wheel in the roller tube with a bolt. Depth of the wheel must fit for the motor length. 2. (Drawing 3) Put the motor into roller tube, insert the motor output shaft into the wheel. The dummy club of counter-loop must be inserted the slot. |  | Drawing 2 Drawing 4 Drawing 6 |  |
| Fix motor system 1. (Drawing 4) Connect the support cap and motor head with two flat head bolts. 2. (Drawing 5) Fix the square plate with four bolts. Atten the motor adjust konb holes must face outside, in order to adjust the travel more easy after installation. 3. (Drawing 6) Put the motor head with support cap into the bracket, then fix well with two pins, avoid the motor loosing from the bracket. 4. (Drawing 7) Install the roller tube into idler bracket. |  |  |  |

Power connection

Travel setting

Attention:

1. You must set the travel after the whole system (including the drapery) has been installed.

2. Direction A and direction B are motor directions. Drapery direction sometimes differs with motor direction cause installation.

3. Please set the konb with 323507 travel stick.

Travel setting steps

1. Let the motor turn to direction A, motor will stop at the scheduled point.

2. Adjust Dir. A konb with travel adjust pen:

If the motor doesn’t reach the order-point, adjust Dir. A konb to “+” direction, the motor will run discontinuously, still reach to the order-point.

If the motor overrun the order-point, adjust Dir. A hole to “-” direction，at this moment, you must run the motor direction B sufficient, and then run direction A again.

3. According to above method, adjust [Dir. B knob] to set the Dir. B travel.

4. If you want to set the order-point accurately, you can drive the motor several times, and then set the travel fine cause the order-point difference.