TA35 AC tubular motor Instruction

Motor Specifications

| Motor type | Voltage | Frequency | Current | Power | Torque | Rotary speed | Maximum travel |
| --- | --- | --- | --- | --- | --- | --- | --- |
| TA35-4/22 | 230V | 50/60Hz | 0.7A | 130W | 4Nm | 22/26rpm | 36turns |
| TA35-6/22 | 230V | 50/60Hz | 0.8A | 150W | 6Nm | 22/26rpm | 36turns |
| Insulation CL Class F protection index IP44 Overheating protection 4min. |

Motor connection Methods

Limit setting

There are two limit knobs on the motor head, which are used to set the limits of direction A and direction B.

Attention

1． Please set the limit after the whole system

installed (including the whole blind system).

2． Direction A and direction B are the turning directions of the output shaft of motor. Sometimes these two directions are the same with the blind moving direction, sometimes different. So please do not refer the blind moving direction as the motor turning direction.

Setting steps

1．Operate the motor on direction A. It will stop automatically when it reaches the pre-establish stop point.

2. Use adjust pen to adjust direction A knob to set the stop point.

If the current stop point does not reach the aim stop point, please adjust direction  knob A on the direction “+”. During the moment of adjustment, the motor will move following the scope of adjustment till the motor reaches the aim stop point.

If the current stop point is over the aim stop point, please adjust direction knob A on the direction “-”. At this time you should operate the motor to move a little on the direction B. Then operate the motor to turn on the direction A again. The motor will reach the stop point which adjusted.

3．According to the up steps, please set the direction B through direction knob B.

4．If the more exact stop point requested, please operate the motor up and down at the whole limit several times, and look round the stop point. If necessary, please jiggle the limit according to the step 2.